## Slide 1
Autonomous Underwater Vehicle (auv) guidance digital control
December 2022
ALEX KHAIR AND JUSTIN HART
The University of Texas at Austin

## Slide 2
Introduction
Objectives
Equation of Motion/State Space Representation
Inputs/Controllability
Emulation/Block Diagram
Results
Conclusions
Future Work
OVERVIEW
2

## Slide 3
  AUVs are unmanned underwater robots that operate independently from humans
  Industries served – oil and gas, defense, oceanographic research/exploration
  Research under work  experimenting with different models/controllers to find best solution
INTRODUCTION
3

## Slide 4
OBJECTIVES
Replicate and study trajectory tracking of an AUV
  Derive 6 DOF plant model
  Utilize PID controllers to control the 3 controllable inputs to the AUV
  Emulate the system (controllers + plant) in the discrete time
Investigate system performance qualitatively
  Sampling rate effect on stability
  Ability to track different trajectories
  Robustness against different disturbances
4

## Slide 5
Equations Of Motion
Plane Model Matrices
Hydrodynamic/Hydrostatic Forces Acting on the Body
Disturbances
Inputs
States
5

## Slide 6
Nonlinear State Space Representation
The 6 DOF plant model allows for 12 states: the 6 velocities (3 linear and 3 angular) and 6 positions (3 cartesian coordinates and 3 angles)
Coordinate Frame Transformations
Overall State Equation
6

## Slide 7
Inputs/Controllability
System isn’t fully controllable
  12 states
  5 non-zero inputs to the system
  3 controllable inputs
No control over roll
Propellor Speed
  Indirectly controls the velocity states
Rudder Angle
  Controls the yaw angle
  Lift force acts perpendicular to the plane of the rudder ()
    Produces a moment about
Stern Planes
  Controls the pitch angle
  Lift force acts perpendicular to the stern planes ()
    Produces a moment about
7

## Slide 8
Block Diagram
8

## Slide 9
Performance Metrics
Sideslip angle Beta [1]
Is the system stable?
Can it track different trajectories?
  Propellor revolution ramped to 1525 rpm and held
  Depth ramped to 30 m and maintained (max operational of depth 100 m)
  Trajectory 1: Ramp yaw angle to constant value and hold
  Trajectory 2: Yaw angle sine wave path following
  Trajectory 3: Constant ramping yaw angle from (spinning about z)
Is system robust against disturbances?
  Ocean current speed
    Realistic: 0.5 m/s (average current velocity at ocean surface [3])
    Worst Case: 1.8 m/s (average current velocity of the gulf stream [4])
  Ocean Current sideslip angle
    Fixed: constant value of 33 (orthogonal to vessel at final yaw position of trajectory 1)
    Worst Case: Varying angle to always remain orthogonal to the vessel
9

## Slide 10
Results: Sampling Time Analysis
T = 0.05s (20Hz)
T = 0.15s (6.67Hz)
Criteria
  Computational efficient (reasonable run time)
  Stable
Identified through guess/check tuning
  Ideal sampling time of .05 seconds
  Instability arises at sampling time of .15 seconds
10

## Slide 11
Results: Trajectory 1, Constant , Variable Current Speeds
Reasonable Current (.5 m/s)
Fast Current (1.8 m/s)
11

## Slide 12
Results: Trajectory 1, Continued
Reasonable Current (.5 m/s)
Fast Current (1.8 m/s)
Plant Inputs
Velocity States
12

## Slide 13
Results: Trajectory 2, Constant , Fast Current
  Note controller failed to track worst case angle
Position/Angle States
Plant Inputs
13

## Slide 14
Results: Trajectory 3, Constant , Fast Current
  Note controller failed to track worst case angle
Position/Angle States
Plant Inputs
14

## Slide 15
Results: Density Parameter Study
Nonuniform Density
Uniform Density
15

## Slide 16
CONCLUSIONS
Successfully rederived a 6 DOF, realistic, nonlinear plant model for an AUV
  Represented the model in terms of nonlinear state equations
    Reduced the second order system to a first order system
  Emulated the model using ODE45 function in MATLAB
Demonstrated ability to track reference profiles for all 3 controllable inputs using discrete time PID controllers
  Inputs were moved sequentially
  Capable of tracking various yaw angle trajectories
Demonstrated robustness of the system against various disturbances
  Evaluated tracking capability for different current speeds
  Evaluated tracking capability for different horizontal angles of current flow
16

## Slide 17
FUTURE WORK
Lyapunov stability
  Reference [1] has a discussion on this for similar systems
Elaborate upon input profiles/disturbances
  Investigate performance when providing inputs concurrently
  Define trajectories in terms of cartesian x and y coordinates in the NED frame
    Model their relationships to controllable inputs
  Evaluate effects of vertical current streams
Dive deeper into the controller model
  Investigate adaptive PID coefficients
  Investigate optimal control methods
More thorough parameter study
  Define quantitative performance metrics
17

## Slide 18
QUESTIONS?
18

## Slide 19
References
[1] Fossen, T. I. (2021). Handbook of Marine Craft Hydrodynamics and Motion Control (2nd ed.). Wiley.
[2] Imlay, F. H. (1961). The Complete Expressions for Added Mass of a Rigid Body Moving in an Ideal
Fluid. Technical Report DTMB 1528. David Taylor Model Basin. Washington D.C.
[3] “Ocean Current.” Encyclopædia Britannica, Encyclopædia Britannica, Inc., https://www.britannica.com/science/ocean-current.
[4] US Department of Commerce, National Oceanic and Atmospheric Administration. “How Fast Is the Gulf Stream?” NOAA's National Ocean Service, 1 June 2013, https://oceanservice.noaa.gov/facts/gulfstreamspeed.html.
19